## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – PS26073
Problem Statement Title– AI/ML based anomaly detection in Automatic Weather Station data
Theme– <THEME AS LISTED ON THE SIH PORTAL>
PS Category- Software
Team ID– <TEAM ID>
Team Name (Registered on portal)– <TEAM NAME>

## Slide 2: SKYGUARD: AWS DATA QUALITY CONTROL
Proposed Solution (Describe your Idea/Solution/Prototype)
Detailed explanation of the proposed solution
Four stages: remove the expected daily and seasonal cycle, compare the station against its nearest neighbours, score what is left with an unsupervised model, then name the likely fault from its shape.
Uses only the three fields the problem statement provides — temperature, pressure and relative humidity. No extra instrument is assumed.
Two tiers: a physical-plausibility screen on the station node itself, and everything that needs neighbouring stations on one server.
How it addresses the problem
Separates a faulty sensor from real weather by asking whether the neighbouring stations moved in the same direction at the same time.
Every alert names a probable cause with a confidence — stuck probe, drift, step offset, dropout — instead of raising a bare flag.
Alert volume is held to a fixed budget per station per week, so the output stays small enough for an operator to actually read.
Innovation and uniqueness of the solution
The baseline is frozen on an approved reference window and never refitted on live data: a self-updating baseline quietly absorbs slow drift and hides the very fault it should expose.
Dew point is used as a physical cross-check — heating a probe raises temperature and lowers humidity but leaves dew point where it was, which separates a shield or siting fault from genuinely warmer air.
Answering “unknown” when the evidence supports no cause is a designed output, not a failure.
Your Team Name

## Slide 3: TECHNICAL APPROACH
Technologies to be used (e.g. programming languages, frameworks, hardware)
Python — NumPy, pandas and scikit-learn for the residual, detection and classification stages. No GPU and no model server.
FastAPI service with a browser operator console; Leaflet map on satellite imagery with the official India boundary served by NCMRWF (MoES).
Station node: ESP32-class microcontroller with a BME280 temperature / pressure / humidity sensor. PostgreSQL with TimescaleDB for storage.
Methodology and process for implementation (Flow Charts/Images/ working prototype)
The station tier holds only constant-size state, so no history buffer or model runtime is needed on the node; thresholds are calibrated on a clean reference period before deployment.
Your Team Name
STATION NODE
range · rate · stuck-value screen
REMOVE CYCLE
frozen daily + seasonal baseline
COMPARE NEIGHBOURS
did nearby stations move too?
SCORE
unsupervised, fixed alert budget
NAME + EXPLAIN
cause, confidence, or “unknown”

## Slide 4: FEASIBILITY AND VIABILITY
Analysis of the feasibility of the idea
A national network at 15-minute reporting is only a few records per second — one modest on-premise VM handles it with no GPU.
Methods are established and inspectable: robust regression, neighbour differencing, unsupervised scoring. Not a black box.
The station tier is inexpensive and runs on hardware already common in AWS deployments.
Potential challenges and risks
Station density — neighbour comparison only works where a nearby station is correlated enough to serve as a reference.
Genuine severe weather can look like a fault, risking false alarms during exactly the events that matter most.
Slow calibration drift never looks like an outlier at any single moment.
Alert fatigue: a system that flags too much gets switched off.
Strategies
Measure how inter-station differences grow with distance first, and let that measurement choose each station's neighbours.
Gate alerts on neighbour agreement, so a change the whole region shares reads as weather rather than a fault.
Freeze the baseline on approved data and track drift as a divergence growing over days, never from a single reading.
Cap alerts to a fixed budget per station-week, and abstain when uncertain.
Your Team Name

## Slide 5: IMPACT AND BENEFITS
Potential impact on the target audience
IMD and MoES network operators get a ranked, named list of the stations needing attention, instead of raw observation streams to inspect.
Forecasting and numerical weather prediction gain cleaner input: bad observations are caught before they are assimilated.
Field maintenance is directed to the station that is actually faulty, and to the sensor within it.
Benefits of the solution (social, economic, environmental, etc.)
Social — warnings and forecasts that reach the public rest on observations checked for sensor faults.
Economic — fewer wasted site visits, and instrument replacement planned from evidence of degradation rather than a fixed cycle.
Environmental — the node transmits only flagged readings and a periodic health summary; radio transmission dominates an AWS power budget, so a quieter uplink means a smaller power system.
Institutional — a long-term record whose quality is documented, which matters for climate-scale reuse of the archive.
Your Team Name

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
IMD — M. N. Ranalkar et al., “Quality control of Automatic Weather Station data”, MAUSAM 66(1), 2015: the checks IMD applies today, including the spatial regression test.
IMD Vision 2047 (press release, 14 Jan 2025) — smart weather stations, AI for real-time quality control, and self-diagnosing instruments: internal.imd.gov.in/press_release/20250114_pr_3552.pdf
NCMRWF Technical Report NMRF/TR/02/2022 — observation quality control and buddy checks in the operational assimilation system.
NCMRWF operational dashboard and model guidance: nwp.ncmrwf.gov.in
WMO-No. 8, Guide to Instruments and Methods of Observation (CIMO Guide) — measurement uncertainty and siting classification.
ECMWF ERA5 reanalysis via the Copernicus Climate Data Store — reference fields used to develop and test the method.
Your Team Name